## Slide 1: GIS Workshop

## Slide 2: Intro to GIS
Basic GIS Concepts
Layers
Spatial/Non Spatial Information
Topology

## Slide 3: Intro to GIS
Basic GIS Concepts
GIS datasets are organized into layers defined by category and data type
Each GIS dataset requires an individual layer
User can then overlay, view and analyze composite maps
Layers are turned on and off by the user, as needed
  In most GIS interfaces, the user can control how the layers are stacked (i.e., which layers can be seen, which layers are buried under others, how layer transparency is used)

## Slide 4
Spatial / Non-Spatial
Basic GIS Concepts
GIS includes both spatial and non-spatial information
Spatial data includes geometry and location of layers.
Non-spatial data is typically called attribute data. Stored in a database and used for answering spatial questions (queries).
Spatial and non-spatial data for specific geographic features are linked by unique identifiers.
This is called the Georelational Model.

## Slide 5: Georelational Model (Vector Features)
Attribute Table
Geographic Features
Points
Lines
Polygons
Records (rows)
Fields (columns)
One record for each geographic feature

## Slide 6
Topology is a branch of mathematics concerned with the location of objects, in space, relative to each other.
A GIS topology is a set of rules and behaviors governing how points, lines and polygons share geometry.
        (ESRI 2005)
Topology
Basic GIS Concepts

## Slide 7
Contiguity | Connectivity | Containment
Concepts of Topology Used in GIS
Topology
Basic GIS Concepts

## Slide 8
Adjacent features share common edges (e.g. municipalities, parcels, land cover)
Contiguity
Examples

## Slide 9
Network analysis (e.g., streets, sewer/water systems, stream systems)
(Source: www.esri.com)
Connectivity
Examples

## Slide 10
Spatial analysis (e.g., buffer, spatial join)
(Source: www.esri.com)
Containment
Examples

## Slide 11: What You Need to Know About a GIS dataset
Any data layers to be used together in analysis, should be represented in the same:
    Projection
    Coordinate system
    Coordinate reference system
    Datum (Geoid, Spheroid, Ellipsoid and “realization”)

## Slide 12: Map Projection
Map Projection - An orderly method used to represent all or part of a 3D globe on a 2D map.

## Slide 13
Los Angeles
New York
Los Angeles
New York
Projection: Mercator Distance: 3,124.67 miles
Projection: Albers Equal Area Distance: 2,455.03 miles
Map Projections

## Slide 14: Just a Reminder…
Most GIS analysis tools are designed to work with Cartesian coordinates, rather than latitude and longitude.
“It is wise to be careful when using a GIS to analyze data in latitude and longitude rather than in projected coordinates, because serious distortions of distance, area and other properties may result.”
(Longley, p. 119)

## Slide 15
Area Class (Unique Value)
Choropleth
Dot Density
Graduated Symbol/Color
Proportional Symbol
Thematic Maps
Map Types - Many Different Kinds; a few examples:

## Slide 16
In addition to “data types” the GIS user needs to be aware of the “levels of measurement” of the attribute data:
  Nominal – Objects are classified into groups.
  Ordinal – Uses concept of order – objects can be sorted.
  Interval – Object is placed on a number line with an arbitrary zero point and an arbitrary interval.
  Ratio – True origin and arbitrary interval. Can be used in arithmetic operations of addition, subtraction, multiplication and division.
Data Classification Levels of Measurement

## Slide 17
Natural Breaks: Appropriate for non-normal distributions (default in ArcGIS).
Equal Interval: Appropriate for an even (uniform) or normal distribution.
Standard Deviation: Appropriate for a normal distribution.
Quantile: Appropriate for a uniform or normal distribution.
Defined Interval: Appropriate for an even (uniform) or normal distribution.
Data Classification Classification Methods

## Slide 18: Map Elements Appear on Most Maps
Title
Legend
Map body
Scale
Labels
Direction indicator
Source

## Slide 19: Joins
To join two tables, the primary key and the foreign key must have EXACTLY the same data type and (to be safe) field width. The field width is not an issue with recent ArcGIS versions, but may be with other applications.
The most common reason that two tables do not join properly is that the user has not made the two key fields match PERFECTLY in data type.

## Slide 20: Two tables

## Slide 21: One joined table

## Slide 22: Spatial Join
8
We often have point datasets to which we would like to attach the attributes of the polygons from another dataset.
Example:
  We have a point dataset for Section 8 housing units in a city. We would like to attach attributes from the enclosing Census block group for each point.

## Slide 23: Point in Polygon Analysis
9
In ArcMap 10.x, if you want to “stamp” a point dataset with the attributes of the polygon (in another dataset) that the points fall in, you use the “Join” command.
  Right-click on the point layer.
  Use the “Join” tool.
  Then go to “Join data from another layer based on spatial location”.

## Slide 24
+
=
Spatial Join
Join Polygons to Points

## Slide 25: Join Polygons to Points
11

## Slide 26
12
+
=
Spatial Join
Join Points to Polygon

## Slide 27: Join Points to Polygon
13

## Slide 28: Find Features with Particular Attributes
Use Select by Attribute
First, right-click on a layer and set it to be the only selectable layer.
Next, we use an SQL query on the attribute table.
A dialog box interface helps us build our SQL query.

## Slide 29: Tabular/Attribute Query: Boolean Logic
Search for 'SQL reference' in the ArcGIS Desktop Help

## Slide 30: Query Operators Access & ArcGIS
= (equal sign)
<> (not equal to)
Like (inexact searches, with wildcards)
> (greater than)
< (less than)
>= (greater than or equal to)
<= (less than or equal to)
And
Or
Not
Is Null
Is Not Null

## Slide 31: Boolean Logic or Set Theory
XOR
(somewhat expansive)

## Slide 32: Selecting Features
Click on the “Select Features” tool. The default is a rectangle graphic. Make a small box on each feature you want to select. Hold down the Shift key to select more than one feature.
We will complete a hands-on exercise to learn other selection methods.

## Slide 33: Selection Tools
Select by attribute This is the same as querying from a table
Select by location This tool allows you to select features from layers that meet specified criteria relative to the features in another layer.
Select by graphics From the Draw Toolbar, select a graphic. Use the Select Elements tool, and select the features you want with the graphic. Then use the Selection drop-down menu, and Select by Graphics.

## Slide 34: Spatial Query Examples
3
Point-in-polygon: What is the total employment of large employers (points) in New Brunswick (polygon)? How many bus stops (points) are there within our study area (polygon)?
Line-in-polygon: How many miles of bus routes (line) are within Mercer County (polygon)?
Polygon-in-polygon: Retrieve data for the census block groups (polygons) within the Central Business District (polygon).

## Slide 35: Select by Location
4
Select by Location
Statistics

## Slide 36: Spatial Query Examples
5
Radius/buffer search
  Identify all children (points) within a 1 mile radius of a school (buffer around a point).
  Identify all large employers (points) within a 1/4 mile distance of a bus route (buffer around a line).
  Notify all property owners within 1000 feet of a proposed liquor license (buffer around a polygon).

## Slide 37
6
Select by Location

## Slide 38: Geoprocessing Tools
16
DATA MANAGEMENT: GENERAL
          Merge, Append
DATA MANAGEMENT: GENERALIZATION
          Dissolve
ANALYSIS: EXTRACT
          Clip, Select
ANALYSIS: PROXIMITY
          Buffer, Near
ANALYSIS: OVERLAY
          Intersect, Union, Identity
          Erase, Symmetrical Difference

## Slide 39: Merge Tool
ArcToolbox:
Data Management Tools, General Toolset.
Combines input features from multiple sources of the same type

## Slide 40: Clip Tool - Polygons
In ArcToolbox, in
Analysis Tools, in
Extract.

## Slide 41: Clip Tool - Lines

## Slide 42: Buffer Tool
Point
Line
Polygon
In ArcToolbox, Analysis Tools, Proximity Toolset

## Slide 43: Intersect Tool
In ArcToolbox,
Analysis Toolbox,
Overlay Toolset

## Slide 44: Data Type
.SHP: Shapefile. The primary file of GIS. Contains all of spatial data on it.
.DBF: The file can be opened in Excel. Documented data of attribute table.

## Slide 45
Hand-on Exercise

## Slide 46: Launch ArcGIS

## Slide 47: ArcGIS Interface- Catalog
Browse and find geographic datasets to add to your map.
Record, view, and manage datasets and ArcGIS documents.
Search for and discover GIS data on local networks and the Web.
Define, export, and import geodatabase data models and datasets.
Create and manage the schemas of geodatabases.
Add connection to and administer ArcSDE geodatabases.
Add connection to and administer an ArcGIS server.

## Slide 48
Use the Connect to Folder tool to make connections to data folders on servers and to your own workspaces.
Make a Connection
ArcGIS Interface

## Slide 49: Connect ‘ W2_ScaleGeneration’ folder and ‘W8_Join Middlesex ‘ folder

## Slide 50: ArcMap: Table of Contents
Open from Windows dropdown. Pin to left-hand side of map window.
Layers draw from the bottom up.
User can move layers up and down in the drawing order.
List by drawing order, List by source
ArcGIS Interface

## Slide 52: ArcMap: Standard Toolbar
Add toolbars from the Customize dropdown, then Toolbars.
ArcGIS Interface

## Slide 53: Select Features

## Slide 54: Selection- by Attribute/by location

## Slide 55
Generate a Map

## Slide 56
Generate a Map

## Slide 57: Join data from excel file
Open W8_Join Middlesex folder